## Slide 1
QLA right-angle
SMA to
BNC

## Slide 2
Ctune (left group). Cmatch (right group).
Tune Ct and Cm. If Center frequency is high, add capacitance to Ct.
Daughter Board:
  Ideal Dimensions: 1cm x 1cm
  Set traces to 0.125” width
  Make vias 2-3x larger for stability.
  0.1” header pins (gold plated)
  Capacitors: 100 – 1000pF
  Capacitor Footprint:
    Passive components – 2225C footprint is (1.8 x 6.6mm).
      Order 25x of 1500pf, 1800pF, 2200pF, 2700pF.
      Part #: 2225C[cap_code]KP501X
      Cap_code = 152 (1500pF), 182 (1800pF), 222 (2200pF), 272 (2700pF).
Motherboard:
  Dimensions:
  Ground plane: should this cover entire board?
Metal Enclosure:
  Enclosure dimensions:
    Check RF lab (backroom, lower cabinets) for metal enclosures.
  SMA pigtail soldered to board, convert to BNC, leave male end dangling to go to TRA switch.
  Possible inputs to motherboard:
    Right-angle QLA input ()
  Ground enclosure

## Slide 3
Daughter Board (top)
C1
C2
C3
Daughter Board (bottom)
P1
P2
P3
P4
Header Pins
(male)
Mother Board (top)
QLA
(right-angle)
SMA to BNC
(Via to
Ground Plane)
Header Pins
(female)